Cost Estimate for CHOOZ2 Veto Shield

Victor Guarino

HEP-ANL

May 4, 2005

- Basis of Estimate

This cost estimate is based on the following assumptions:

  - All modules will be 32 scintillator (41.5mm wide strips) wide which results in a module width of 1,330mm.  This is four strips wider than the largest  MINOS modules.  All of the modules will be 1,330mm wide by 5,320mm long

  - All of the modules will have the same manifolds.

  - Near Detector cylinder Diameter is approximately 9m.  A 10m x 10m square will cover the top.  There are four layers.

  - Far detector will just have a 2.6m x 10m cover.

  - MINOS costs were used as a basis for estimate, however, these costs were increased because we will not get the economies of scale and special deals from universities that MINOS received.  Fabrication/scintillator costs were increased by 50%.

The figures below show the basic layout of the cylinder and top modules for the near detector

- Number of Modules

There will be the following number of modules.

Near detector

- Top will have 16 modules per layer - 48 modules total

- Cylinder will have 24 modules per vertical layer - 48 modules total

- Cylinder will have 24 modules per horizontal layer - 48 modules total

Far Detector

- Top will have 4 modules per layer - total 16 modules

Total number of modules = 160

- Costs

The basis for the costs is:  $990/module + $575/meter

Therefore, a single module will cost $4,050 /each.

| Item | Unit Cost | Quantity | Cost |
| --- | --- | --- | --- |
| Module | $4,050 | 160 | $648k |
| Factory Equipment |  |  | $150,000 |
| Module Shipping |  |  | $6,000 |
| Design and Construction of Support Structure |  |  | $120,000 |
| Total |  |  | $924k |